## Slide 1
EAVN WS
2015/710@Hokkaido University
Millimeter Interferometer Collaboration Experiment 2015
(MICE2015)
Kenta FUJISAWA (Yamaguchi University)

## Slide 2: Japanese short mm-VLBI activity
230 GHz test VLBI in Japan
To obtain fringes and engineering experiment
EHT
Honma et al.
Caravan
Miyoshi et al.
Balloon
Doi et al.
Universities
Institutes

## Slide 3: All Japan mmVLBI team
ISAS/JAXA
Observation strategy, OCXO
NAOJ
Mizusawa VLBI Observatory
Observation strategy, OCXO
Kyoto University
Scientific advices
Osaka Prefecture University
Telescopes, receiver and observing system
Yamaguchi University
Organization of this ‘team’
Ibaraki University
Equipment, arrangement
NICT Kashima
VLBI terminal, data reduction, 10MHz reference transfer
NAOJ
Nobeyama Radio Observatory
Infrastructure for Observation

## Slide 4: Outline of the experiment
Purpose
  Engineering experiment at the highest frequency so far
  Fringe detection (no image, no science, but engineering)
Experiment
  Date: April 27, 2015 (started in February!)
  Place: Nobeyama Radio Observatory
  Telescope: SPART 10m, 1.85m
    Owned/operated by Osaka Pref U for single dish observation
  Frequency: 230.000-231.024 GHz
  Source: Edge of the Moon
  VLBI terminal: NICT, NAOJ, ISAS/JAXA, Ibaraki, Yamaguchi
  Correlation: GICO3 software correlator by NICT
4

## Slide 5: 230 GHz VLBI at Nobeyama
150 m
(VSBI)
© 国立天文台
Osaka Pref U
1.85m telescope
Osaka Pref U
10m telescope (SPART)
(one of NMA)
Steady 230 GHz observation as single dishes
But
No VLBI back-ends
Need for building VLBI system temporary!

## Slide 6
10m SPART
Telescope
D/C
LO Sum
230.0 GHz
Sampler
GALAS
PC
GPS受信機
(NTK )
1PPS Generator
ECHO AQ-3300
10MHz distributor
…
OCXO
TIC
Agilent 53131A
cntl
1PPS
10MHz
+10dBm
1PPS
1PPS
Cabin
Observation Room
1.85m
Telescope
GPS
Spectrometer
DISK
Ref RX
LAN
(Private)
IF 0-2 GHz
0 dBm (?)
Ref 10MHz
10 dBm
D/C
LO Sum
230.0 GHz
Cabin
Spectrometer
10←5
GPS
1PPS Gen
Comparator
H-maser
Sampler
GALAS
PC
cntl
DISK
LAN
(FIXED IP)
10MHz distrib
Ref TX
45m bldg
IB
IF 0-1 GHz
0 dBm (?)
Ref 10MHz
10 dBm
Optical fiber
Lay on groung
240m （need protection）
Coaxial cable
2 lines of 30m on ground
（need protection）
Cable path to inside of building
Cabling
GPS
TIC
5 MHz
1 PPS
Polarization
LHCP or RHCP
l/4 plate off
For Linear Pol
Installation of equipments
１．Ntp connection
２．ftp data transfer
Power line
Coaxial cables
connectors
230GHz VLBI Experiment
(MICE2015) 2013/04/23 KF
Power meter
Spectrum analyzer
tester
OCXO
Source: the Moon
tracking: change the tracking position so that to maximize the correlated amplitude
Calibration
Tsys measurement
Frequency 230.000-231.024 GHz
no Doppler tracking
CO (2-1) line included so that to check the frequency setting
1.85m: USB, SPART: DSB
1.85m: circular pol, SPART: linear pol
Correlation: ftp just after the recording
Power off the amplifier
Before pulling cable off
Frequency setting?
Frequency setting?
Confirmation of tracking
And 10 MHz reference
Station Position ?
茨城大
山口大
NICT
NAOJ/ISAS
大阪府大／NRO
Build for this experiment

## Slide 7: Three Reference Signal Modes
[Mode 1] Connected interferometer mode
  10 MHz transfer via optical fiber
[Mode 2] H-maser (SPART) --- OCXO (1.85m)
[Mode 3] OCXO (SPART) --- OCXO (1.85m)
OCXO
  Oven Controlled Xtal Oscillator
  Good Stability at 230 GHz for 10 seconds integration
  Cheap and compact (transportable)

## Slide 8: Optical fiber
Fiber route for200m cable
protection
Pulling out from a duct

## Slide 9: VLBI back-end for 1.85m
Optical fiber transceiver
Sampler (Galas by NICT)
K6 recording server
(RAID behind the server)

## Slide 10: Back-end for SPART
Sampler (Galas)
K6 recording server

## Slide 11: First 230 GHz fringe in Japan !
16k point / 100 Hz fringe search window

## Slide 12
H-maser --- OCXO
OCXO --- OCXO
OCXOs showed good performance!

## Slide 13: What’ Next ?
1. International Experiment 2. Scientific Observation
SPART 10m
NRO 45m
230 GHz Rx install??
Korean telescope??
Chinese telescope??
SMA ??
JCMT ??
EHT ??
NRO 45m
86 GHz
KVN 86GHz??

## Slide 14
East-Asian VLBI Network
Short mm-VLBI in East Asia?
KVN-NRO45m＠86GHz?