## Slide 1: CVN software correlator development and its applications
Zheng Weimin*, Zhang Juan, Tong Li, Tong Fengxian, Liu Lei,
Chen Zhong, Shu Fengchun, Wang Guangli
Shanghai Astronomical Observatory,
Chinese Academy of Sciences
8th East Asia VLBI workshop, Sapporo, Japan
8 - 10 July, 2015

## Slide 2: Outline
Development history
Applications in CE-3 mission
Development status
Future work
CVN software correlator

## Slide 3: 1. Development history
2003-2004
First CVN software correlator: Satellite Fringe searcher
Matlab
First domestic Geostationary, Elliptical Orbit Satellites VLBI correlation
2004-2007
FX type software correlator for Chinese Lunar Exploration Project (CE-1)
c language
ESA SMART-1, TC-1, TC-2 VLBI tracking experiment
Hardware correlator debugger & backup in CE-1 preparation stage
SMP parallelization

## Slide 4
2007-2010
Primary CVN correlator in CE-1, CE-2 lunar projects
Near real time correlator, with satellite fringe search ability
Data latency < 2min
VLBI center latency ~ 6min
2011-2015
Primary correlator in CE-3, CE-5T1 projects
Real time correlation & satellite fringe search ability
MPI + OpenMP parallelization
Data latency < 10sec
VLBI center latency < 40sec
2011-2013
CVN Geodesy application of Crustal Movement Observation Network of China (CMONOC )

## Slide 5: Outline
Development history
Applications in CE-3 mission
Development status
The future work
CVN software correlator

## Slide 6: CE-3 Mission objective: 2. Applications in CE-3 mission
Complete the Chinese first soft-landing and roving exploration on the Moon (first probe to soft-land on the Moon since Luna 24 in 1976)
Demonstrate and develop key technologies for future missions.
Scientific objectives:
Lunar surface topography, lunar surface material composition and resource survey, lunar-based astronomical observation, etc.

## Slide 7: New Requirements & techniques of CVN
High accuracy
Real time ability
Accurate Moon surface positioning
Combined orbit determination
( X band ΔDOR )
DOR – Differential of One-way Range
( e-VLBI + real time data process pipleline)
(Same Beam VLBI, SBI )
(2-way/ 3-way range + VLBI)

## Slide 8
  Mission Requirements on VLBI
Earth-Moon transfer orbit phase & circumlunar phase
ΔDOR tracking group delay < 4ns (Actuality <0.5ns)
Orbit & angular determination and orbit prediction；
System data processing latency < 1minute (Actuality 15~40 seconds)
Lunar surface working phase
Lander & Rover tracking by SBI
Lander 3D position <1km (Actuality <100m )
Rover relative position of the lander <500m (Actuality ~1m )

## Slide 9: CVN data center real-time pipelines in CE-3

## Slide 10: Block diagram software correlator
NFS: Network File System

## Slide 11: Computing platform
Standard Linux cluster
Five I/O nodes
- E7-4820*4/ 128GB/ 300GB+12TB
32 compute nodes*12 cores
fringe search + correlation
- E5-2640*2/ 32GB/ 300GB
2 manage nodes
- E5-2620*2/ 24GB/ 900GB+214GB
Management network
- 10G Ethernet
Compute network
- InfiniBand

## Slide 12: Specifications of CE-3 software correlator
Processing Mode | Real-time & post-processing
Station number | 1~20
Real-time fast fringe search | 4 stations
IF number | 1,2,4,8,16
Frequency channel | 24~16384/IF
Integration period | 0.1~60 second
Maximum data speed (192 CPU cores) | About 1.9Gbps/station, totally 4 stations
Output format | CVN, FITS-IDI

## Slide 13
  Rover positioning by same-beam VLBI
Differenced VLBI group delay Real time mode
Same beam phase reference image
postprocess mode
Differenced VLBI phase delay, postprocess

## Slide 14: Null test by same beam phase reference image positioning
Local coordinate | North | East | Down | Distance
Same-beam phase-referencing VLBI result | 1.197 | -0.005 | -0.759 | 1.417
True value | 1.016 | -0.605 | -0.759 | 1.405
Differences | 0.181 | 0.600 | 0.000 | 0.012
Null test error:
~ 0.6 m

## Slide 15
Rover
A
B
C
D
E
E17

## Slide 16: Outline
Development history
Applications in CE-3 mission
Development status
The future work
CVN software correlator

## Slide 17: 3. Development status
Increase correlation speed by MPI+Pthreads
6 stations * 1.1Gbps/station->2.0Gbps/station
192 CPU cores
GPU acceleration: VGOS application
Geodesy application: Output format CVN--> Mk4,
Pulsar gate : Pulsar processing

## Slide 18: CVN to Mark4 format transform test
Via DiFX software package
  cvn2difx: developed by our group
  difx2mark4: provided by DiFX
Direct convert
  cvn2mark4: under development
CVN visibility output
delay model
cvn2difx
DiFX SWIN format
.im file
.input, .calc, .flag
difx2mark4
Mark4 format
type-0 (root)
type-1 (corel)
type-3 (station)
.vex
vex2difx
CVN visibility output
delay model
cvn2mark4
Mark4 format
type-0 (root)
type-1 (corel)
type-3 (station)
.vex

## Slide 19
CVN
DiFX

## Slide 20: DiFX vs. CVN SC

## Slide 21: GPU acceleration correlator prototype
Two GPU Nodes
Each node:1 x Nvidia K40c
GPU Workstation | DELL T5600
Chipset | Intel C600
CPU | Intel E5-2600 @ 2.00GHz
Memory | 64GB
Ethernet | Intel 82579 1Gb NIC
Infiniband | Mellonax ConnectX 40Gb/s QDR
GPU | NVIDIA Kepler K40c

## Slide 22: CE-3 DOR delay difference: GPU SC vs. CPU SC
GPU | Speed/station
1 node | 337Mbps
2 nodes | 670Mbps
Four station speed test
NVIDA K40C

## Slide 23
20s integration without pulsar gate and dispersion correction
Pulsar B0329+54 preliminary result
20s integration with pulsar gate and dispersion correction

## Slide 24: 4. Future work
CVN needs a general purpose software correlator:
Lunar and deep space exploration mission
Geodesy and astronomy data processing
Pulsar binning, multi-phase center ability
VGOS broadband ability
New software correlator
CVN, IVS(VGOS), EVAN, AOV

## Slide 25
Thank you for your attention!

## Slide 26
Rover position （4 ways）
Site |  | Visual+ Inertial navigation | VLBI group delay | VLBI phase delay | VLBI phase reference map
A | N | 9.03 | -4.2 | 11.25 | 9.47
 | E | 1.55 | .4 | 1.28 | 1.15
B | N | 5.00 | -269.8 | 5.89 | 5.12
 | E | 8.90 | -640.8 | 7.56 | 9.30
C | N | -5.65 | 80.5 | -4.92 | -5.34
 | E | 8.36 | 10.0 | 8.02 | 8.86
D | N | -9.75 | 112.6 | -8.73 | -9.51
 | E | 0.27 | 69.2 | 0.37 | 0.49
E | N | -19.77 | 59.0 | -17.35m | -19.26
 | E | -0.20 | 32.0 | -0.42 | -0.29
E17 | N | -11.83 | / | / | -11.063
 | E | -13.05 | / | / | -12.961

## Slide 27: Residual statistics
Chart: VLBI Delay Data Fit（unit: ns）
| 41610 | 41611 | 41612 | 41613 | 41614 | 41615 | 41616 | 41617 | 41618 | 41619 | 41620 | 41621
real-time | 0.8 | 0.8 | 0.5148 | 1.0012 | 0.72667 | 0.65853 | 0.68263 | 0.71603 | 0.62713 | 0.5331 | 0.421 | 0.37717
VLBI group delay residuals：
~ 1ns in trans-lunar orbit
~ 0.5ns in lunar orbit.

## Slide 28
Fast fringe search is closed!
Fast fringe search is opened!
The result of CVN software correlator using the fast fringe search function. The show tool is real-time monitoring tool developed by ourselves.

## Slide 29: Perilune braking real time fringe search result